Safe Operating Procedure – Receipt and Despatch of Loan Kits

| Description of Task | PACKING AND UNPACKING SURGICAL LOAN SET TRANSPORT CASES |
| --- | --- |
| Identified Risk | Musculoskeletal Disorder – Shoulder, neck, upper limb and lower back strain |
| Safety Controls | Mechanical lifting device must be used at all times Training – in SOPs for the safe use of mechanical aids. Prepare workstations and surrounds, e.g.: How and where it arrives and leaves. |
| Precautions to be exercised | Consider body positioning while sliding trays in and out of the transport cases – minimise twisting and turning Recommended tray weight of 5-7kgs (for trays over this weight, decant ) Lifting device to be connected to AC outlet for recharging daily. |
| Training and Competency | Completion of competency-based manual handling training re SOPs; equipment; etc. Address individual needs where applicable Ongoing workplace assessment by M/H Co-ordinator and/or nominated competent person |
| Supervision | Implementation of buddy system Ongoing workplace supervision by M/H Co-ordinator and/or nominated competent person |
| Relevant Legislation and Standards | NSW – Work Health and Safety Act 2011 NSW - Work Health and Safety Regulation 2011 Code of Practice – Hazardous Manual Tasks National Guide for the Safe Design and Handling of Surgical Instrument Transport Cases (2011) |
| Information and Resources | Health Service Organisation [HSO] Orientation Team Meetings Safe Operating Procedure/s [SOP] must be displayed in appropriate area/s. |

Safe Operating Procedure – RECEIPT OF LOAN KITS

| TASK: UNPACKING LOAN SURGICAL INSTRUMENT SETS FROM NEW TRANSPORT CASES |
| --- |
| Prior to commencing task, complete Health and Safety checklist for work environment, refer to pre-start checklists |
| Instruct courier to deliver stacked loan kit/s on wheeled platform/s to designated receipt area that contains: Appropriate lifting device (fixed / mobile) |  |
| Adjustable workstation with roller/s positioned facing lifting device |  |
| Delivery receipt documented as per hospital policy |  |
| Wheel stacked loan kits to unpacking / processing area and onto fixed or mobile lifter (located beside adjustable workbench). |  |
| Ensure brakes are applied (if mobile lifter) |  |
| Ensure case/s are secured onto the wheeled platform (dolly). |  |

| TASK: UNPACKING LOAN SURGICAL INSTRUMENT SETS FROM NEW TRANSPORT CASES continued |
| --- |
| Open door of transport case/s and secure into ‘open’ position using stretch loop. |  |
| Raise / lower lifting device so that the instrument tray (to be unloaded from transport case) is at workstation height |  |
| Slide instrument tray from transport case onto workstation. Decant as necessary. Check instrument tray against original order (following QA procedures) |  |
| Identify instrument tray as per HSO protocols for reprocessing |  |
| Using workstation rollers, transfer instrument trays and required instruments onto washer disinfector trolley (or equivalent) for transfer to cleaning process. |  |
| Using lifting device, adjust height of transport case to remove the next instrument tray. |  |
| Repeat process for each instrument tray until transport case is empty. *slip sheets to remain in transport case– do not remove during unpacking process. Return outer trays to container. Identify transport case for packing and despatch |  |
| Transfer empty transport case/s to designated holding area. Remove any unnecessary labelling and stack containers for storage using your risk assessment protocols |  |

Safe Operating Procedure – DESPATCH OF LOAN KITS

| TASK: PACKING LOAN SURGICAL INSTRUMENT SETS INTO NEW TRANSPORT CASES FOR DESPATCH |
| --- |
| Prior to commencing task, complete Health and Safety checklist for work environment; refer to pre-start checklists |
| Transport case/s on their wheeled platform (dolly) from designated holding area to loan set area |  |
| Securely position the mechanical lifter under the road case’s wheeled platform |  |
| Using lifter, raise the container |  |
| Unlock door and secure door in open position, align mechanical lifter to the workstation and ensure brakes are applied (if mobile lifter) |  |
| Once terminal process has taken place, wheel instrument trays on mobile trolley/ to loan set area. Transfer each tray with instruments onto workbench (with roller/s). |
| Check out instrument trays as per HSO policy and manufacturer’s instructions |
| Ensure each lid is secured onto tray |
| Ensure heaviest trays are positioned lowest in case (and heaviest cases are positioned lowest in stack) |
| Leaving one slip-sheet at the base, remove extra slip sheets from transport case to workstation. |
| Slide first tray into transport case, via rollers. |
| Use lifter to raise / lower cases so that individual trays are loaded at workbench height. |

TASK: PACKING LOAN SURGICAL INSTRUMENT SETS INTO NEW TRANSPORT CASES FOR DESPATCH continued

Slide and position the next slip sheet on top of that tray in the transport case.

Repeat process until transport case is full. (Any un-used slide sheets can be re-positioned above the top tray inside the transport case)

Enclose all relevant documentation as per HSO policy.

Securely lock and label each case

Using mechanical lifter, collect pre-packed prosthesis tubs and place on top of wheeled container ready for collection (see picture below)

Wheel transport cases to be picked up by courier in the designated despatch area

Complete despatch documentation as per HSO policy